## Slide 1: Radio-Interferometric Measurement Equation Introductory Radio Interferometry Course Radio Astronomy Techniques and Technologies Group (RATT) Rhodes University
Modhurita Mitra
February 18, 2015

## Slide 2: Radio-Interferometric Measurement Equation (RIME)
Compact, intuitive, matrix-based way of representing propagation effects in radio interferometry.
Useful for calibration (solving for and correcting these propagation effects).

## Slide 3: Introduction
in reference frame of sky, at the source
(linearly or circularly polarized)
Propagation effects
Antenna
Source
in reference frame of sky, at the observer
Can be represented
as vectors:

## Slide 4: Propagation effects absent
No propagation effects
Antenna
Source
Amplitude and direction of electric vector
remain unchanged during propagation

## Slide 5: Propagation effects present
Propagation effects
Antenna
Source
Linear transformation matrix,
Jones matrix
Electric field vector
Voltage vector
Amplitude and direction of electric vector
change during propagation

## Slide 6: Correlation
Antenna p
Source
Antenna q
Correlator

## Slide 7: Visibility
The correlator computes the visibility, , on the baseline :
Hermitian conjugate
Outer product
Average
= 2
These 4 quantities are the outputs from the correlator

## Slide 8: Correlation
,

## Slide 9: Coherency, or Brightness
By definition, the coherency, or brightness, B, is given by:
=
is the coherence of the electromagnetic field with itself,
and is described by the Stokes parameters

## Slide 10: Radio-Interferometric Measurement Equation (RIME)
Visibility
Brightness
Jones matrices

## Slide 11: Component Jones matrices
The Jones matrix for an antenna is a product of several component Jones
matrices, corresponding to different corrupting effects along the signal path
Parallactic angle
feed rotation
Instrumental
gain
Bandpass
gain
Polarization
leakage
Ionospheric
Faraday rotation
Primary
beam
Example:

## Slide 12: Component Jones matrices
Jones chain:
Later
in signal path
Earlier
in signal path

## Slide 13: Component Jones matrices
Propagation effects
Antenna
Source
Jones matrix,
Earlier
in signal path
Later
in signal path

## Slide 14: Component Jones matrices
Antenna p :
Antenna q :
Visibility
Brightness
Jones matrices

## Slide 15: Calibration
Calibration: Determining and correcting for propagation effects
in order to compute the brightness.
i.e., solve for Jones matrices to compute :
Visibility
Brightness
Jones matrices

## Slide 16: Direction-independent and direction-dependent effects
Propagation effects can be of two kinds:
Direction-independent effects
Direction-dependent effects
These effects can be represented by different Jones matrices:
Final Jones matrix
Direction-independent
effects
Direction-dependent
effects

## Slide 17: Direction-independent and direction-dependent effects
Final Jones matrix
Direction-independent
effects
Direction-dependent
effects
Visibility-plane effects
Image-plane effects

## Slide 18: Direction-independent and direction-dependent effects
Parallactic angle
feed rotation
Instrumental
gain
Bandpass
gain
Polarization
leakage
Ionospheric
Faraday rotation
Primary
beam
Direction-independent
effects
Direction-dependent
effect

## Slide 19: Direction-independent effects
Antenna
Source 1
Same in all directions
Source 2

## Slide 20: Direction-dependent effects
Antenna
Source 1
Source 2
Varies with direction

## Slide 21: Structure of Jones matrices
Most Jones matrices have a simple form:
(in a circularly polarized basis)

## Slide 22: Rotation matrices
Examples:
Parallactic angle feed rotation:
Ionospheric Faraday rotation:
Parallactic angle
Faraday rotation angle

## Slide 23: Leakage matrices
Examples:
Polarization leakage:
Polarization leakage terms

## Slide 24: Gain matrices
Examples:
Instrumental gain:
Bandpass gain:

## Slide 25: Direction dependent effects: Primary beam
The primary beam of the antenna is the most important
direction-dependent effect.
Becomes important in wide-field, wide-band observations.
The primary beam pattern has a multiplicative effect in the
image plane, convolutional effect in the visibility plane.
We will consider the example of a JVLA (Jansky Very Large Array)
antenna here.

## Slide 26: Primary beam amplitude variation with distance from center
Distance
Beam gain
Horizontal cross-section of the beam
through the center

## Slide 27: JVLA primary beam
1⁰
Main lobe
First null
First sidelobe
(at 1410 MHz)

## Slide 28: Primary beam rotation
An EVLA antenna has an alt-azimuth mount;
the primary beam rotates during the course of an observation

## Slide 29: Variation of primary beam with frequency
Frequency
Beam gain
The beam pattern becomes more compact
with increasing frequency
Beam-induced spectral variation
for the source represented by a dot

## Slide 30: Incorporating primary beam in calibration
Calibration without primary beam included
Calibration with primary beam included
EVLA image of the field around the radio source 3C147

## Slide 31: Effect of primary beam on noise over the field of view
EVLA image of the field around the radio source 3C147

## Slide 32: Calibration procedure
Start with visibility data,, and initial brightness model, .
Solve for .
Calculate residual visibility data .
Image to create a residual image, .
Perform a source-finding procedure to find sources in the residual image, and add these to the initial model to form a new, updated model .
Set = , and repeat steps 2-5 until the residual image is noise-like.

## Slide 33: Differential gains
Differential gain solutions encompass the unknown and unmodeled direction-dependent effects in the signal path.
The Jones matrix in the direction of source is then given by:
Final Jones matrix
in the direction
of source s
Direction-independent
effects
Known and modeled
direction-dependent
effects
Differential gain:
Unknown/unmodeled
direction-dependent
effects in the direction
of source s

## Slide 34: Differential gains
Differential gain solutions are computed (in the direction of a few bright sources) and applied after regular calibration in order to correct for leftover, uncalibrated effects.

## Slide 35: Incorporating differential gains in calibration
Without differential gain solutions
(Without primary beam incorporated in calibration)
With differential gain solutions applied

## Slide 36: Differential gains
As more corrupting effects are modeled and accounted for, the calibration becomes more comprehensive, and differential gain solutions approach unity.

## Slide 37: Incorporating primary beam in calibration
Differential gain plots
Flattened differential gain curves,
over the whole range
Residual variation due to
remaining uncorrected direction-dependent
effects (like antenna pointing errors)
Without primary beam
With primary beam
Time
Differential gain
amplitude
Differential gain
amplitude
Time
0
1
2
0
1
2

## Slide 38: References
Thompson, A. R., Moran, J. M., and Swenson, Jr., G. W. (2001), Interferometry and Synthesis in Radio Astronomy, 2nd Edition
G. B. Taylor, C. L. Carilli, & R. A. Perley, editors (1999), Synthesis Imaging in Radio Astronomy II, volume 180 of Astronomical Society of the Paciﬁc Conference Series
14th Synthesis Imaging Workshop lecture slides (2014), National Radio Astronomy Observatory, Socorro, New Mexico, USA
Oleg Smirnov’s RIME lecture from 3GC3 Workshop and Interferometry School (2013), Port Alfred, South Africa

## Slide 39: References (continued)
Smirnov, O. M. (2011). Revisiting the radio interferometer measurement equation. I. A full-sky Jones formalism. Astronomy & Astrophysics, Volume 527, A106
Smirnov, O. M. (2011). Revisiting the radio interferometer measurement equation. II. Calibration and direction-dependent effects. Astronomy & Astrophysics, Volume 527, A107
Smirnov, O. M. (2011). Revisiting the radio interferometer measurement equation. III. Addressing direction-dependent effects in 21 cm WSRT observations of 3C 147. Astronomy & Astrophysics, Volume 527, A108

## Slide 40: References (continued)
Hamaker, J. P., Bregman, J. D., and Sault, R. J. (1996). Understanding radio polarimetry. I. Mathematical foundations. A&AS, 117, 137–147
Sault, R. J., Hamaker, J. P., and Bregman, J. D. (1996). Understanding radio polarimetry. II. Instrumental calibration of an interferometer array. A&AS, 117, 149–159
Hamaker, J. P. and Bregman, J. D. (1996). Understanding radio polarimetry. III. Interpreting the IAU/IEEE deﬁnitions of the Stokes parameters. A&AS, 117, 161–165
Hamaker, J. P. (2000). Understanding radio polarimetry. IV. The full-coherency analogue of scalar self-calibration: Self-alignment, dynamic range and polarimetric ﬁdelity. A&AS, 143, 515–534